Internet of Things
with Arduino

---
Very Basic Circuit Primer
- circuits
  - involves a power source with negative and positive poles
  - electricity flows through and performs work
- types of electricity:
  - alternating current (AC)
    - wall outlets
    - better at transmitting power over long distances
    - Tesla
  - direct current (DC)
    - electronics
    - Edison

---
Very Basic Electronics Primer
- Voltage (volt) – potential difference between two poles of a power source, used for inputs
- Ampere (amp) – measurement of the number of electrons flowing through a circuit
- Wattage (watt) – measure of how much power is consumed, calculated by multiplying volts and amps
- Resistance (ohms) – slows down electricity
- water tank analogy

---
Analog and Digital
- analog
  - works with the full range of available voltage
  - easy to use with input sensors
- digital – on or off
  - what exactly is on or off?
  - circuits not exact
  - voltage
  - some point divides on and off, about 3V for 5V Arduino boards

---
DC Components
- all circuits consist of discrete components
  - Light Emitting Diodes (LEDs)
  - Resistors
  - Transistors
  - Capacitors
  - Potentiometers
  - Buttons
  - Motors
- anode and cathode

---
Arduino History
- started in 2005 at Interaction Design Institute Ivrea in Ivrea, Italy
- began in response to students only having BASIC stamp microcontrollers
  - expensive, around $100
  - program in BASIC
- designed to be simple and inexpensive

---
Arduino Boards
- microcontroller/single board computer vs microprocessor
- not system on a chip (SoC)
- no operating system
- open source hardware
  - plans available online
  - anyone can build
- very basic, low level
- extensible through shields
- can do analog and digital I/O
  - input/output pins for discrete components
  - serial over USB
  - Ethernet/WiFi via shields, ethernet built-in to some boards
- many different models both 5 volt and 3.3 volt
Arduino Boards

---
Input/Output
- Digital Input – high or low
  - high is reading of >= 3 volts (on 5 volt boards)
- Digital Output – high or low
  - depends on board voltage
- Analog Input
  - 0 to 1024
  - max 10,000 reads per second
- Analog Output
  - 0 to 255
  - via Pulse Width Modulation (PWM)

---
Arduino Uno
(Reference Implementation)

---
Arduino Specs
- Uno
  - $23 for official, $11 for generic
  - 2KB RAM, 16MHz, 32KB program space
- Mega
  - $38 for official, $14 for generic
  - 8KB RAM, 16MHz, 256KB program space
  - on board ethernet
  - more input/output pins
- Intel Galileo
  - $50
  - 256MB RAM, 400MHz, 8MB program space
  - on board ethernet

---
Other Single Board Computers
- Raspberry Pi
  - designed as an inexpensive Linux computer
  - not great for hardware hacking
  - $40, 512MB RAM, 700MHz
- Beaglebone Black
  - Linux/javascript
  - $55, 512MB RAM, 1GHz ARM processor
- Tessel
  - javascript/WiFi built-in
  - not intended for hardware hacking
  - $100 (includes expansion module)
  - 32MB RAM, 180MHz ARM processor

---
Getting Started
- Electronics Books (library)
- Arduino Starter Kits
  - sparkfun
  - amazon.com
- digital multimeter
  - autoranging if in the budget
- solderless breadboard
  - often comes with started kit
  - will want bigger