Internet of Things
with Arduino

---
Very Basic Circuit Primer
- circuits
  - involves a power source with negative and positive poles
  - electricity flows through and performs work
- types of electricity:
  - alternating current (AC)
    - wall outlets
    - better at transmitting power over long distances
    - Tesla
- direct current (DC)
    - electronics
    - Edison

---
Very Basic Electronics Primer
- Voltage (volt) – potential difference between two poles of a power source
- Ampere (amp) – measurement of the number of electrons flowing through a circuit
- Wattage (watt) – measure of how much power is consumed, calculated by multiplying volts and amps
- Resistance (ohms) – slows down electricity

---
Analog and Digital
- analog
  - works with the full range of available voltage
- digital – on or off
  - what exactly is on or off?
  - voltage
  - circuits not exact
  - some point divides on and off, about 3V for 5V Arduino boards

---
DC Components
- all circuits consist of discrete components
- Light Emitting Diodes (LEDs)
- Resistors
- Transistors
- Capacitors
- Potentiometers
- Buttons
- Motors

---
Arduino Boards
- microcontroller/single board computer vs microprocessor
- not system on a chip (SoC)
- open source hardware
  - plans available online
  - anyone can build
- very basic, low level
- can do analog and digital I/O
- extensible through shields
- many different models both 5 volt and 3.3 volt
Arduino Boards

---
Arduino History
- started in 2005 at Interaction Design Institute Ivrea in Ivrea, Italy
- began in response to students only having BASIC stamp microcontrollers
  - expensive, around $100
  - program in BASIC
- designed to be simple and inexpensive

---
Arduino Uno
(Reference Implementation)

---
Input/Output
- Digital Input – high or low
  - high is reading of >= 3 volts (on 5 volt boards)
- Digital Output – high or low
  - depends on board voltage
- Analog Input
  - 0 to 1024
  - max 10,000 reads per second
- Analog Output
  - 0 to 255
  - via Pulse Width Modulation (PWM)

---
Arduino Models
Name	Volts	CPU (Mhz)	Program Space (KB)	SRAM (KB)	EE PROM (KB)	Ethernet	Analog In Ports	Digital Ports (IO/PWM)
Uno	5	16	32	2	1	shield	6	14/6
Ethernet	5	16	32	2	1	on board	6	14/6
Mega	5	16	256	8	4	on board	16	54/15
Due	3.3	84	512	96	0	shield	12	54/12
LilyPad USB	3.3	8	32	2.5	1	n/a	4	9/4
Intel Galileo	5	400	8MB	256MB	11	on board	6	14/6

---
Getting Started
- Electronics Books (library)
- Arduino Starter Kits
  - sparkfun
  - amazon.com
- digital multimeter
  - autoranging if in the budget
- solderless breadboard
  - often comes with started kit
  - will want bigger

---
Other Single Board Computers
- Raspberry Pi
  - designed as an inexpensive Linux computer
  - not great for hardware hacking
  - $40, 512MB RAM, 700MHz
- Beaglebone Black
  - Linux/javascript
  - $55, 512MB RAM, 1GHz ARM processor
- Tessel
  - javascript/WiFi built-in
  - not intended for hardware hacking
  - $100 (includes expansion module)
  - 32MB RAM, 180MHz ARM processor